## Slide 1: Parallel and Distributed Computing Module 1-Parallelism Fundamentals

## Slide 2: Outline
Motivation
Key Concepts
Challenges
Parallel computing
Flynn‘s Taxonomy
Multi-core Processors,
Shared vs Distributed memory.

## Slide 3: Motivation
To address computationally intensive problems and increase their response time
Weather Forecasting
Genome Sequencing
Crash Simulation Testing

## Slide 4: Moore’s Law
Transistor count on a integerated chip doubles every 24 months independent of technology used
  @Gordon Moore, Co-founder of Intel Corp (1965)

## Slide 5: Moore’s Law
Pipelined functional units: instruction level parallelism
Superscalar architecture
Out-of-order execution
Larger Caches

## Slide 6: Moore’s Law
More complexity will not lead to more efficiency
More functional units are packed into CPU
The higher probability that the “average” code will not be able to use them
  As the number of independent instructions in a sequential instruction stream is limited.
Faster clock boosts power dissipation making idling transistors useless

## Slide 7: Power-Performance Dilemma
Simplify processor design
Additional transistors for larger cache
So, multi-core processors came into existence

## Slide 8: Parallelization
Misconception: More hardware Faster Response Time
Billions of CPU hours wasted
Supercomputer users have no idea about limitations of parallel execution

## Slide 9: Classes of Parallelism
Data-Level Parallelism (DLP) : Huge data can be operated in parallel
Task-Level Parallelism (TLP) : independent and large tasks in parallel on at the same time.

## Slide 10: Ways to exploit parallelism
Instruction-Level Parallelism:
  Exploit data-level parallelism
  Pipelining
Vector Architectures and Graphic Processor Units (GPUs)
  Exploit data-level parallelism
  Applies a single instruction to a collection of data in parallel.

## Slide 11: Ways to exploit parallelism
Thread-Level Parallelism
  Exploits either data-level parallelism or task-level parallelism
  Allows for interaction among parallel threads.
Request-Level Parallelism
  Exploits parallelism among largely decoupled tasks
  Specified by the programmer or the operating system.

## Slide 12: Flynn’s Taxonomy
These 4 ways to support the data-level parallelism and task-level parallelism for hardware [50 years back].
When Michael Flynn [1966] found a simple classification whose abbreviations we still use today.
SISD
SIMD
MISD
MIMD

## Slide 13: Single instruction stream, single data stream (SISD)
This category is the uniprocessor.
No exploitation of parallelism
Can have concurrent processing
Pipelined and super scalar processors
INSTRUCTION
STREAM
DATA
STREAM
Processing Unit

## Slide 14: Single instruction stream, multiple data streams (SIMD)
INSTRUCTION STREAM
DATA
STREAM1
Processing Unit
DATA
STREAM 2
DATA
STREAM 3
Processing Unit
Processing Unit
DATA

## Slide 15: Multiple instruction streams, single data stream (MISD)
INSTRUCTION STREAM
DATA
STREAM
Processing Unit
Processing Unit
Processing Unit
InstructionStream1
InstructionStream2
InstructionStream3

## Slide 16: MIMD
INSTRUCTION STREAM
Processing Unit
Processing Unit
Processing Unit
InstructionStream1
InstructionStream2
InstructionStream3
DATA
STREAM1
DATA
STREAM 2
DATA
STREAM 3
DATA

## Slide 17: Parallel Scalability
Factors limit parallel execution
Scalability metrics
Scalability Laws:
  Amdahl’s Law
  Gustafson’s Law
Parallel efficiency

## Slide 18: Factors that limit parallelism
1
3
4
5
6
7
2
12
11
10
9
8
1
3
4
2
5
6
7
8
12
11
10
9
W1
W2
W3
Time
Time
Top: Sequence of tasks that needs to be parallelized
Bottom: 3 workers (W1,W2,W3) are used to parallelize the tasks with the time reduction

## Slide 19
But it will not be true and the factor is load imbalance
Some of the resources will be under utilized
Communication between co-workers
Tools to be shared by the co-workers
These factors will add overhead which will serialize some part of parallel execution

## Slide 20: Load imbalance
Tasks will be executed by the workers at different speeds because of load imbalance
Regions indicate that unused regions
1
3
4
2
5
6
7
8
12
11
10
9
W1
W2
W3
Time

## Slide 21: Scalability Metrics
Algorithmic limitations because of mutual dependencies
Bottlenecks because of shared resources
Startup Overhead
Communication

## Slide 22: Run-time
For fixed problem to be solved by N workers,
The single worker run time,
The N-workers run time,
Where S is amount of work can be serialized and P is amount of work that can be parallelized

## Slide 23: Scalability Laws
Application speed up is defined as quotient of parallel and serial performance for fixed problem size
Performance can be defined as “work done over time”
Serial Performance, = 1
Parallel Performance,

## Slide 24: Amdahl’s Law
Gene Amdahl, application speed up is limited to 1/s when N tends to infinite
“What is the improvement in runtime of an application run when the problem is put on N CPUs?”
Serial performance,
Parallel Performance,
Speed up =

## Slide 25: Problems
Bob is given the job to write a program that will get a speedup of 3.8 on 4 processors.
He makes it 95% parallel, and goes home dreaming of a big pay raise.
Using Amdahl’s law, and assuming the problem size is the same as the serial version, and ignoring communication costs, what speedup will Bob actually get?

## Slide 26: Gustafson’s Law
“How much more work can my program do in a given amount of time when I put a larger problem on CPUs?”
Where 0 < < 1, is number of workers,

## Slide 27: Parallel Efficiency

## Slide 28: Multi-core Processors
Cores on a die can have separate caches or shared caches at certain levels
Sharing cache will reduce latency and improve bandwidth for communication between core
But it may lead to cache bandwidth bottlenecks
Recent multicore designs have integrated memory controller which is connected directly to memory modules without chipset
This reduce main memory latency and allows addition of Hyper Transport or Quick Path inter-socket networks
Efficient cache coherence communication

## Slide 29: Dual core Processor
Separate L1, L2, and L3 Cahes
Intel Monticeto
P
L1D
L2
L3
P
L1D
L2
L3

## Slide 30: Quad Core Processor
Two Dual core processors with Shared L1, Separate L2 (Intel Harpertown)
P
L1D
P
L1D
L2
P
L1D
P
L1D
L2

## Slide 31: Hexa core processor
Shared L2, separate L3
L2 groups are dual cores and L3 group is whole chip
Intel Dunnigton
P
L1D
P
L1D
P
L1D
L3
P
L1D
L2
P
L1D
L2
P
L1D
L2

## Slide 32: Quad Core Processor
Separate L1 and L2 caches
Shared L3 cache
L3 group is whole chip
Built-in memory interface allows to attach memory and other sockets without chipset
AMD Shangai and Intel Nehalem
P
L1D
P
L1D
L3
P
L1D
L2
P
L1D
L2
Memory Interface
HT/QPI
L2
L2

## Slide 33: Shared-memory
A system where the number of CPUs work on the physical address space
Two varieties:
  Uniform Memory Access (UMA)
  Cache Coherent Non-Uniform Memory Access (ccNUMA)

## Slide 34: UMA
Known as Symmetric Multi Processing (SMP)
Latency and Bandwidth are the same for all the processors
Simplest implementation is Dual-core

## Slide 35: UMA System with two Single-core chips
Chipset
Memory
P
L1D
L2
P
L1D
L2
Socket
Common Front Side Bus (FSB)

## Slide 36: UMA System with two Dual-core chips
P
L1D
P
L1D
L2
Chipset
Memory
P
L1D
P
L1D
L2
Socket

## Slide 37: Cache Coherence
Cache coherence mechanism is required
Because of same copy of cache line is resided in in several caches
If one of those caches get modified, other cache content needs to be reflected

## Slide 38: MESI Protocol
M: modified
E: exclusive
S: shared
I: invalid
P1
C1
A1 A2
P2
C2
A1 A2
3
7
Memory
A1
A2

## Slide 39
1. C1 requests exclusive CL ownership
2. set CL in C2 to state I
3. CL has state E in C1 → modify A1 in C1 and set to state M
4. C2 requests exclusive CL ownership
5. evict CL from C1 and set to state I
6. load CL to C2 and set to state E
7. modify A2 in C2 and set to state M in C2
P1
C1
A1 A2
P2
C2
A1 A2
3
7
Memory
A1
A2
Courtesy: Hager, G. (2017). Introduction To high performance computing for scientists and engineers: CRC press

## Slide 40: ccNUMA System
P
L1D
P
L1D
L3
P
L1D
L2
P
L1D
L2
L2
L2
Memory Interface
Memory
P
L1D
P
L1D
L3
P
L1D
L2
P
L1D
L2
L2
L2
Memory Interface
Memory
Coherent
Link

## Slide 41: Distributed Memory
P
C
M
NI
P
C
M
NI
P
C
M
NI
P
C
M
NI
Communication Network
P-Processor
C-Cache
NI-Network Interface
M-Memory

## Slide 42: Reference
Hager, G. (2017). Introduction To high performance computing for scientists and engineers: CRC press.
Peterson and Hennesy. Computer architecture: a quantitative approach, 5th edition