## Slide 1: Module 1 : Parallelism Fundamentals

## Slide 2: Motivation
With respect to both hardware and software,
  Road blocks to improve performance with serial code / single uni-core systems
  Hardware has to support parallelism for improved performance
  Software has to be able to offer parallelism (in terms of codes, compilers etc)

## Slide 3: Key Concepts

## Slide 4: What is parallelism?
Parallelism is the process of executing multiple
  Instructions on same data or single instruction on multiple data or a combination of both
Is parallelism and concurrency the same?
  Concurrency does not need redundant units while parallel computing involves redundant structures

## Slide 5: Why Parallelism?
It is the obvious choice of high performance evolution
A learning from applications
  Concurrency and parallelism is key to future systems

## Slide 6: Why Parallel, Concurrent and Distributed Computing?
Parallel computing can transform science and engineering
Example: Cosmology - the study of the universe
  Its evolution and structure—where one of the most striking paradigm shifts has occurred. A number of new, tremendously detailed observations deep into the universe are available from such instruments as the Hubble Space Telescope and the Digital Sky Survey. However, until recently, it has been difficult, except in relatively simple circumstances, to use mathematical theories of the early universe to allow comparison with observations.
  Scalable parallel computers with large memories have changed all of that

## Slide 7: To port or not to port?
That should not suffix (porting)
Write parallel applications for parallel architectures should involve reformulating data structures, basic code and the dynamics involved

## Slide 8: Parallel supercomputing can answer challenges to society
Parallel computing that not only involves particle studies but for human related data
  Health care
  Weather / environmental application

## Slide 9: The burden is not on the ‘Hardware’ alone
Even with existing architecture, there are lot of ways the parallelism can be adapted to harness efficiency in terms of execution time, power and so on

## Slide 10: Overview of Parallel Computing, Architectural Demands and Trends

## Slide 11: Evolution of Parallel architecture
Stored Program Concept
ILP (Pipelining) (SISD)
TLP
OOP (Out-of Order Processors)
Vector Processors (SIMD)
Simultaneous Multi-Threading (SMT)
Multi-core Processors (MIMD)
SIMT Architectures (GPU)
Multi-node systems (With multiple cores, GPUetc) Distributed

## Slide 12: Stored Program Computers

## Slide 13: CPU Fundamentals
Primary function is to execute Instructions
Program Execution Steps
  CPU transfers instructions and i/p data from main memory to registers in the CPU
  CPU executes instruction in their stored sequence (unless altered explicitly)
  CPU transfers o/p data from CPU registers to main memory

## Slide 14: Program Execution

## Slide 15: Single Core Processors

## Slide 16: Single-core computer

## Slide 17: Un-pipelined Data Path

## Slide 18: Single Processor Core
Two Parts : Control Unit and Data Path
Data Path
Control Unit
  Unit to control the Data path

## Slide 19: Pipelining

## Slide 20: Pipelined Data-path
Include Registers in between to provide ILP (hardware support)

## Slide 21: Pipeline Hazards
Structural Hazards
Data Hazards
Control Hazards

## Slide 23: Pipeline Hazards & Solutions
Structural Hazards
  Redundancy
Data Hazards
  Forwarding, Loop Unrolling
Control Hazards
  Branch Prediction

## Slide 24: Constraints in In-order Execution
Data Hazard
DIV.D F0,F2,F4
ADD.D F6,F0,F8
SUB.D F1,F3,F5
MUL.D F6,F10,F8
Structural Hazard
DIV.D F0,F2,F4
DIV.D F1,F3,F5
ADD.D F7,F9,F11
SUB.D F8,F10,F14
MUL.D F6,F10,F8

## Slide 25: …Continued
Control Hazard
Beq F0,F2, S1
DIV.D F1,F3,F5
ADD.D F6,F0,F8
Jmp S2
S1: SUB.D F8,F10,F14
S2: MUL.D F7,F11,F9

## Slide 26: Pipelined Processor with Out of Order Execution
The fundamental problem we face when trying to keep four functional units busy is that it's difficult to find contiguous sets of instructions that can be executed in parallel.
The solution to these problems is out-of-order execution and speculative execution.
Support by both hardware and software
  Hardware that allows instruction execution out of order
  Software to allow totally independent instructions to be fetched

## Slide 27: Drawback of In Order Execution
A major limitation of in order execution is
  Stalling the execution pipeline till all the previous instructions are issued irrespective of its data dependency
    Eg:
        DIV.D F0,F2,F4
        ADD.D F10,F0,F8
        SUB.D F12,F8,F14

## Slide 28: The Idea of Out of Order Execution
In the previous example, to issue SUB.D, we must separate issue into two parts:
  Checking for any structural hazard
  Waiting for the absence of data hazard
We still use in-order instruction issue, but we want an instruction to begin execution as soon as operands are available which implies Out Of Order Completion

## Slide 30
DIV F0, F1, F2
MUL F4, F2, F3
ADD F5, F0, F4
SUB F5, F2, F1
ShiftL F1, F6, F7

## Slide 31: Continued…
Out of order execution introduces the possibility of WAR and WAW hazards which do not exist in the 5-stage pipeline
Eg:
DIV.D F0,F2,F4
ADD.D F6,F0,F8
SUB.D F8,F10,F14
MUL.D F6,F10,F8
  WAR Hazard between ADD.D and SUB.D
  WAW Hazard between ADD.D and MUL.D

## Slide 32: Out-of-Order Completion Complexities
Exceptions should be preserved and imprecise exceptions should not arise.
Imprecise exceptions can occur because of two possibilities
  The pipeline may have already completed instructions that are later in program order than the instruction causing exception
  The pipeline may have not completed some instructions that are earlier in program order than the instruction causing the exception

## Slide 33: Out – of Order Execution
It requires multiple functional units or pipelined functional units or both.
In a dynamically scheduled pipeline, all instructions pass through the issue stage in order
However, they can be stalled or bypass each other in the read operand stage.
Score-Boarding is a technique for allowing instructions out of order execution when there are sufficient resources and data dependences.
Tomasulo’s Algorithm: handles anti-dependences and output dependences by effectively renaming the registers dynamically.

## Slide 34: Evolution of Multi-Core

## Slide 35: Era before Multi-Core
  Improved hardware technologies resulted in,
    Increased clock frequency
    Increased transistor density
    Exploiting ILP

## Slide 36: What is Instruction Level Parallelism?

## Slide 37: Power Wall
Can put more transistors on a chip than afford to turn on

## Slide 38: Frequency Wall
Dynamic power in a chip is proportional to V2fC
So increasing ‘f’ will lead to power wall.

## Slide 39: Memory Wall

## Slide 40: What’s the Solution?
Because of the above discussed walls, performance can no more be benefitted from ILP or by increasing frequency
Improved Thread level Parallelism will provide the solution
Software level threads were developed to increase number of threads

## Slide 41: Software Solution to Improve ILP

## Slide 42: Concurrent Execution Model
More complex computing systems allow a user to run multiple applications that execute at the same time.

## Slide 43: Sequential Execution
Conventional programs are called sequential because a programmer imagines a computer executing the code statement by statement
At any instant, the machine is executing exactly one statement

## Slide 44: Thread Level Parallelism – Increasing Hardware Threads

## Slide 45: How TLP overcomes the barriers?
Overcoming Power wall & Frequency wall
  A single processor operating at 4 GHz can be replaced by a multiple processor each operating at 2 GHz.
Overcoming Memory Wall
  Multithreading means cycle-by-cycle interleaving of instructions from different processes.
  If one process is busy with memory, that latency can be masked by executing other threads.

## Slide 46: Why not Multi-Processors?
Communication latency between processors on different boards are high.
This will become a bottle neck for performance.

## Slide 47: What is Multi-Core?

## Slide 48: Moore’s law : Alive & Well
Gordon Moore (co-founder of Intel) predicted in 1965 that the transistor density of semiconductor chips would double roughly every 18 months.

## Slide 49: Comparison of different architectures
Single Core
Multi-core processor
Multiprocessor
Multi-core processor with shared cache
Multi-core processor with distributed cache

## Slide 50: Goals of Parallelism

## Slide 51: What are the Goals of parallelism?
To make the architectural design scalable
To have improved performance
To Balance cost- performance and reliability

## Slide 52: Have these goals been achieved with multi-core?
To certain extent
The applications are unable to exploit the parallelism available in the multi-core processors
This has to be addressed

## Slide 53: Challenges
To utilize the existing parallel architectures thoroughly
  Skilled people to write parallel programs
  To develop tools and libraries for parallel programming support
To scale the existing systems to perform better for the future
Architectural models to cater to fast and big data computing

## Slide 54: Future Architectures
Future architectures will emphasis not only on the processors but also on
  I/O devices
  Memory
  Interconnection among nodes

## Slide 55: Communication and Co-ordination

## Slide 56: INTERCONNECTION NETWORKS FOR PARALLEL COMPUTERS
Physically Shared Memory

## Slide 57: Distributed Memory

## Slide 58: Network Topologies
Direct Networks
  Direct networks consist of physical interconnection links that connect the nodes (typically PEs) in a parallel computer
    Each node may need a router to make routing decisions.
  Ring
  Mesh

## Slide 59: Continued…
Mesh Torus

## Slide 60: Continued…
Hypercube network

## Slide 61: Continued…
Indirect Networks
  In indirect networks, each processing node is connected to a network of switches over one or more (often bidirectional) links.
  Typically, this network consists of one or more stages of switch boxes

## Slide 64
double arraySum = 7;
for (int i = 0; i < 100; i++) {
arraySum += A[i];
printf(arraySum)
}
arraySum=7
for (i=0 ; i<100;i<100;i=i+3)
{
arraySum+=a[i] (4 clk)
arraySum+=a[i+1] (
arraySum+=a[i+2];
}

## Slide 65
loop3:
load $f10, 0($5) ; $f10 ← A[i]
add $f8, $f8, $f10 ; $f8 ← $f8 + A[i]
addi $5, $5, 8 ; increment ptr for A[i]
addi $7, $7, -1 ; decrement loop count
test:
bgtz $7, loop3 ; Continue if count > 0